## Slide 1: Predicting Biomechanical Outcomes of Sit-to-stand with Direct Collocation
Team members
Mikayla Schneider 👩🔧, Soyong Shin 👨🔧, and Vu Phan 👨🔧
Carnegie Mellon University
Spring 2023
Project Presentation

## Slide 2
Why do we care about sit-to-stand?
Boswell et al., npj Digital Medicine (2023)
Very common in real life
Typical test used by clinicians
Easy to perform

## Slide 3
Our proposal
Record video
📱
Smartphone
OpenPose
Direct collocation
Simulation
Modeling
Video
Reference state
Model
Outcomes
F = m.a
Kinematics
Kinematics
Kinetics
Biomechanics
Joint torques
Forces
Boswell et al., npj Digital Medicine (2023)
Joint angles
Previous approach
Mass, inertia, length, etc. of each body segment
de Leva, Journal of Biomechanics (1996)
Biomechanics
Rajagopal et al., IEEE Transactions on Biomedical Engineering (2016)
Biomechanical constraints, etc.

## Slide 4
Optimal control problem
Tracking cost
Effort cost
OpenPose state
Hip position X (global frame)
Hip position Y (global frame)
Trunk angle (global frame)
Hip angle
Knee angle
Ground reaction forces
Seating forces
Hip torque
Knee torque
subject to
Biomechanical constraints on joint angles and torques
Dynamic constraints
Initial state (sitting)
Final state (standing)

## Slide 5
Results and Discussion
Hip (o)
Knee (o)
Samples
RMSEmodel = 5.11o
RMSEOpenPose = 5.93o
RMSEmodel = 6.49o
RMSEOpenPose = 1.95o
Hip (N.m)
Knee (N.m)
GRF (N)
SF (N)
Joint angles
Joint torques
Forces
Ground truth (from mocap)
Kinematics tracking from OpenPose
Tracking from the dynamic model / y-axis (for forces)
x-axis (for forces)

## Slide 6
Thank you for your listening!
Q&A
Meanwhile, below are our first few attempts before getting it to work 😅
No constraints
No contact
Too much constraints on standing
Too much constraints on sitting
Bad constraints
Future work
Improve the biomechanical model (e.g., foot contact model, biomechanical parameters/constraints, etc.)
Apply to 3-dimensional scenarios